## Slide 1: CS40L25 Boot Buzz Power Up Sequence

## Slide 2: CS40L25 Boot Buzz Power Up Sequence
Parameter | Symbol | Minimum | Typical | Maximum | Unit
Supply Voltage ramp up/down (VP) 0-2.5V | t1 |  |  | 100 | ms
VP high to VA ramp delay | t2 | 0 |  |  | ns
VA high to VRTC (32.768kHz) ramp delay | t3 | 0 |  |  | ns
Delay from 32.768kHz clock source active to RESET_B high | t4 | 0 |  |  | ns
RESET_B High to control port active | t5 |  |  | 750 | us
RESET_B High and VRTC (32.76kHz) to GP Toggle for Boot Buzz | t6 |  |  | 3 | S
Boot Buzz Current Consumption |  |  | 608 |  | uA

## Slide 3: CS40L25 RTP Demo Setup

## Slide 4: CS40L25 I2C Streaming Demo
  Setup
    PC
      Matlab
      WISCE
      Logic Analyzer software
    Lochnagar 2
      CDB40L25 board
    Class-D filter connected to CS40L25 amplifier output
    Logic Analyzer connected to
      CS40L25 I2C pins
      Output of Class-D filter

## Slide 5: CS40L25 I2C Streaming Demo
  Running
    Matlab code
      Opens wav file
      Copies buffer of samples into DSP registers over I2C
      Initiates playback over I2C
    Logic Analyzer shows
      I2C lines with protocol decode
      Amplifier output
    Can see
      Latency from I2C initiation to playback start
      Waveform shape
      Latency measured <1.2ms
      AoH Standby Mode @ 212uA (Register contents preserved)
Driver
DSP FW
Writing into I2C Buffer control
I2C Wake up
Initiate the I2C playback
LRA Transducer
Buffer transfer and up- sampling
Raising an ACK
Waveform playback
Writing into I2C Buffer control
Initiate the I2C playback
Buffer transfer and up- sampling
Waveform playback
Raising an ACK